## Slide 1: Neutrino CP Violation with the European Spallation Source neutrino Super Beam Marcos Dracos IPHC-Strasbourg

## Slide 2: European Spallation Source
under construction phase
(~1.85 B€ facility)
Neutron facility
(equivalent to SNS in the USA)

## Slide 3: Applications of neutrons
Multi-disciplinary science applications
Transmutation of radioactive (waste) material
  Accelerator-driven Systems
Industrial applications:
  materials analysis and non-destructive testing tools in many industries
    heavy mechanical production
    art conservancy
    Medicine
    …
X-Ray Image
Neutron radiograph

## Slide 4: ESS proton linac
The ESS will be a copious source of spallation neutrons.
5 MW average beam power.
125 MW peak power.
14 Hz repetition rate (2.86 ms pulse duration, 1015 protons).
Duty cycle 4%.
2.0 GeV protons
  up to 3.5 GeV with linac upgrades
>2.7x1023 p.o.t/year.
Linac ready by 2025 (full power)
4
8
time (ms)
Brightness (n/cm2/s/sr/Å)
7
5
x1014
UK TS1
128 kW
UK TS2
32 kW
SNS
1-2 MW
JPARC
0.3-1 MW
ILL 57 MW
ESS 5 MW
2015 design
0
1
2
3
3
4
1
2
6
λ = 1.5 Å
ESS 5 MW
2012 design (TDR)
empty space for energy upgrades

## Slide 5: What does it mean 5 MW?
One beam pulse:
    has the same energy as a 16 lb (7.2kg) shot traveling at
    1100 km/hour
    Mach 0.93
And this for 14 pulses/sec…
Many challenging problems to solve.
proton beam
target wheel absorping all hadrons and muons
neutron beam exraction port

## Slide 6: European Spallation Source
Oct. 2020
Klystron Gallery
Cryo Compressor
Building
Central Utility
Building
Distribution
Substation
Target
Monolith
Exp. Hall
E01
Active
Cells
Front End
Building
High Energy
Loading Bay
European Research Infrastructure Consortium (ERIC) since 2015

## Slide 7: European Spallation Source
(courtesy M. Eshraqi)

## Slide 8: ESS schedule
2014
Construction work starts on the site
2009
Decision: ESS will be built in Lund
2025
ESS construction complete
2003
First European design effort of ESS completed
2012
ESS Design Update phase complete
2019
First neutrons on instruments
2023
ESS starts
user program

## Slide 9: European Spallation Source as Neutrino Facility for CP violation observation (2nd Oscillation maximum)
νμ→νe
or, what else can we do with 5 MW proton beam?

## Slide 10: Oscillation probability (neutrino beams)
"solar"
"atmospheric"
"interference"
matter effect
δCP dependence,
sizable matter effect for long baselines
for antimatter: δCP →-δCP and a→-a
fake matter/antimatter asymetry due to matter effect
Matter-antimatter asymmetry

## Slide 11: δCP and matter-antimatter asymmetry magnitude
(Jarlskog invariant)
Theoretical models predict that if |sinδCP|≳0.7 (45°<δCP<135° or 225°<δCP<315°), this could be enough, under assumptions, to explain the observed asymmetry.
(from the already observed CP violation in the hadronic sector)
(Nucl.Phys.B774:1-52,2007, arXiv:hep-ph/0611338)

## Slide 12: Use all this ESS linac power to go to the second oscillation maximum
but why?

## Slide 13: Neutrino Oscillations with "large" θ13
solar
more sensitivity at 2nd oscillation max.
P(νμ→νe)
L/E
1st oscillation maximum
2nd oscillation maximum
θ13=1º
("small" θ13)
θ13=8.8º
("large" θ13)
dCP=-90
dCP=0
dCP=+90
L/E
for small θ13 1st oscillation maximum is better
for "large" θ13 1st oscillation maximum is dominated by atmospheric term
CP interference
CP interference
solar
atmospheric
atmospheric
θ13=1º
θ13=8.8º
(arXiv:1110.4583)
L/E
L/E
solar
1st oscillation max.: A=0.3sinδCP
2nd oscillation max.: A=0.75sinδCP
(see arXiv:1310.5992 and arXiv:0710.0554)
(before 2012)
(after 2012)

## Slide 14: Having access to a powerful proton beam…
What can we do with:
5 MW power
2 GeV energy
14 Hz repetition rate
1015 protons/pulse
>2.7x1023 protons/year
p
π
ν
decay tunnel
proton beam
target
hadrons
hadronic collector
(focusing)
Detector
physics
⨂B
conventional neutrino (super) beam

## Slide 15: ESSνSB ν energy distribution
at 100 km from the target, per year (in absence of oscillations)
neutrinos
anti-neutrinos
almost pure νμ beam
small νe contamination which could be used to measure νe cross-sections in a near detector
(Nucl. Phys. B 885 (2014) 127)

## Slide 16: Can we go to the 2nd oscillation maximum using our proton beam?
Yes, if we place our far detector at around 500 km from the neutrino source.
MEMPHYS like Cherenkov detector
(MEgaton Mass PHYSics studied by LAGUNA)
Neutrino Oscillations
Proton decay
Astroparticles
Understand the gravitational collapsing: galactic SN ν
  Supernovae "relics"
Solar Neutrinos
Atmospheric Neutrinos
500 kt fiducial volume (~20xSuperK)
Readout: ~240k 8” PMTs
30% optical coverage
(arXiv: hep-ex/0607026)
New 20" PMTs with higher QE and cheaper (see JUNO), the detection efficiency will improve the detector performance keeping the price constant, not yet taken into account.

## Slide 17: Neutrinos in the far detector
540 km (2 GeV), 10 years
Below ντ production, almost only QE events, not suffering too much by π0 background.
neutrinos
anti-neutrinos
2 years
8 years
δCP=0

## Slide 18: 2nd Oscillation max. coverage
2nd oscillation max.
well covered by the ESS neutrino spectrum
1st oscillation max.
full coverage of the 2nd oscillation max.

## Slide 19: ESS Linac modifications to produce a neutrino Super Beam
European Spallation Source Linac

## Slide 20: How to add a neutrino facility?
The neutron program must not be affected and if possible synergetic modifications.
Linac modifications: double the rate (14 Hz → 28 Hz), from 4% duty cycle to 8%.
Accumulator (C~400 m) needed to compress to few μs the 2.86 ms proton pulses, affordable by the magnetic horn (350 kA, power consumption, Joule effect)
  H- source (instead of protons),
  space charge problems to be solved.
~300 MeV neutrinos.
Target station.
Underground detector.
Short pulses (~μs) will also allow DAR experiments (as those proposed for SNS) using the neutron target.

## Slide 21: Candidate active mines
Garpenberg mine
  Distance from ESS Lund 540 km
  Depth 1200 m
  Truck access tunnel
Zinkgruvan mine
  Distance from ESS Lund 360 km
  Depth 1500 m
  Truck access tunnel
Granite drill cores
Lund
Zinkgruvan
(360 km)
Garpenberg
(540 km)
Garpenberg
Zinkgruvan
possible location of MEMPHYS in
Zinkgruvan mine

## Slide 22: Which baseline?
~60% δCP coverage at 5 σ C.L.
>75% δCP coverage at 3 σ C.L.
systematic errors: 5%/10% (signal/backg.)
CPV (Nucl. Phys. B 885 (2014) 127)
Zinkgruvan
Garpenberg
Candidate active mines

## Slide 23: Physics Performance (CPV discovery)
little dependence on mass hierarchy,
δCP coverage at 5 σ C.L. up to 60%,
δCP accuracy down to 6° at 0° and 180° (absence of CPV for these two values),
not yet optimized facility,
5/10% systematic errors on signal/background.
540 km

## Slide 24: Physics Performance (accuracy)
5/5 yrs
δCP accuracy down to 6° at 0° and 180°
12° accuracy at δCP= -90° and 10° at δCP= 90°
5/10% systematic errors on signal/background.

## Slide 25: Required modifications of the ESS accelerator for ESSνSB
Better to go to 2.5 GeV

## Slide 26: The Linac modifications and operation
P
P
H-
H-
H-
H-
H-
H-
H-
H-
H-
H-
H-
H-
H-
H-
H-
H-
H-
H-
H-
H-
H-
H-
H-
H-
Into linac
Into ring
Into horn
14 Hz
14 Hz
14 Hz
~1.4 kHz
Horn 1
Horn 2
Horn 4
Horn 3
100 µs
0.65 ms
~1 µs
~0.75 ms
H- source options
time operation option

## Slide 27: The Accumulator
4 superperiods
FODO cells
injection
RF
extraction
collimation
Dispersion-free straight sections
Switchyard
H- stripping
lattice development

## Slide 28: General Layout of the target station
Split Proton Beam
Neutrino Beam Direction
Collimators
Horns and Targets
Decay Volume
(He, 4x4x25 m3)
Beam Dump
8 m concrete
Horn Support Module
Shield Blocks

## Slide 29: Latest Improvements
Genetic Algorithm for Target Station optimisation
New Magriation Matrices compared to those of MEMPHYS
MEMPHYS WC detector
Phys. Rev. ST Accel. Beams 16, 061001 (2013)
~500 kt
new far detector reconstruction algorithm
(publication is coming)
horn optimisation
DEMOKRITOS contribution

## Slide 30: Improvements
360 km
540 km
best version of NF
ESSnuSB
θ12 = 33.44°
θ13 = 8.57°
θ23 = 49.2°
Δm221 = 7.42e-5
Δm231 = +2.517e-3
2nd osc. max.
507 ktons far detector
10 years
EUROnu
θ12 = 33.2°
θ13 = 9.2°
θ23 = 45°
Δm221 = 7.64e-5
Δm231 = +2.45e-3
1st osc. max.
very preliminary
(to be confirmed)
very preliminary
(to be confirmed)
(publication in preparation)

## Slide 31: Improvements (discovery potential)
360 km
540 km
EUROnu performance
discovery potential at the level of the Neutrino Factory!
75% after 10 years
10 years
very preliminary

## Slide 32: Improvements (precision measurements)
very preliminary
EUROnu performance
10 years
360 km
540 km
Precision measurements
ESSnuSB
Neutrino Factory

## Slide 33: Muons at the level of the beam dump
muons at the level of the beam dump
(per proton)
y (cm)
x (cm)
4.2x1020 μ/year
(16.3x1020 for 4 m2)
4.1x1020 μ/year
2.7x1023 p.o.t/year
muons/proton
<Eμ>~0.46 GeV
<Lμ>~2.9 km
10-3
input beam for future 6D m cooling experiments (for muon collider),
low energy nuSTORM,
Neutrino Factory,
Muon Collider.
more than 4x1020 μ/year from ESS compared to 1014 μ used by all experiments up to now (1018 μ for COMET in the future).

## Slide 34: Muons at the level of the beam dump
<Eμ>~0.5 GeV
<Lμ>~3 km
() | ( ) | ( ) | ( ) | ()
decay tunnel length

## Slide 35: ESSνSB and (R&D) synergies
Super Beam
Neutrino Factory
Muon Collider
+Decay At Rest and Coherent scat.
(with short pulses)
nuSTORM
nm or nm
nm + ne
ne + nm
2.7x1023 p.o.t/year

## Slide 36: Muon Collider as Higgs Factory
Carlo Rubbia
arXiv:1908.05664
HIFI Uppsala Workshop 2-3 March 2020

## Slide 37: Muons at ESS (ESSμSB)

## Slide 38: Muons at ESS (ESSμSB)

## Slide 39: Muons at ESS (ESSμSB)

## Slide 40: Low Energy nuSTORM at ESS
Proposed at FERMILAB and CERN (~3.8 GeV muons)
Sterile Neutrino searches
Neutrino cross sections measurements with unprecedented precision
LBL performance improvement by systematic error mitigation
To be adapted for lower muon energies (~0.5 GeV)
preliminar studies for ESS
sterile neutrino searches

## Slide 41: Decay At Rest at ESS
Possible if short pulses (~μs)
A
+
-
~99%
+
e+
p


e
  26 ns
  2.2 μs
Fragments
DAR
capture
Well known neutrino spectra (DAR).
Very high neutrino intensities ~ 5x1015 n/s.
Separate neutrinos of different flavors by time cut.
Role that neutrino-nucleus interactions play in the supernova explosion process and subsequent nucleosynthesis.
Accurate knowledge of neutrino-nucleus cross sections is important (almost no data exist).
This lack of knowledge significantly limits our understanding of supernovae and of terrestrial observations of cosmic neutrinos to probe the deepest layer of these powerful explosions.

## Slide 42: Coherent Scattering at ESS
SNS
sterile neutrinos,
neutrino magnetic moment,
non-standard interactions (NSI) mediated by new particles,
probes of nuclear structure,
improved constraints on the value of the weak nuclear charge,
reduction in neutrino detector mass may lead to a number of technological applications as non-intrusive nuclear reactor monitoring.
CEνNS is also expected to dominate neutrino transport in neutron stars, and during stellar collapse.
…

## Slide 43: Coherent Scattering at ESS
JHEP 02 (2020) 123
ESS can generate the largest pulsed neutrino flux suitable for the detection of Coherent Elastic Neutrino-Nucleus Scattering (CEνNS ).
Innovative detector technologies able to profit from the order-of-magnitude increase in neutrino flux provided by the ESS, along with their sensitivity to a rich particle physics phenomenology accessible through high-statistics, precision CEνNS measurements, are under study.

## Slide 44: Current ESSνSB status
COST Action EuroNuNet (CA15139): ended March 2020
  https://euronunet.in2p3.fr
  video for scientists: https://www.youtube.com/watch?v=PwzNzLQh-Dw
EU-H2020 Design Study ESSνSB: on going up to March 2021 (3 months extension due to COVID19)
  https://essnusb.eu
  video for general public: https://www.youtube.com/watch?v=qAnvft0nAlg

## Slide 45: Design Study ESSνSB (2018-2021)
CDR end of 2021
15 participating organisations within 11 countries
Starting date: 01/01/2018
Ending date: 31/12/2021 → 31/03/2022
Duration: 48 Months
Grant Agreement signature: 22/11/2017
Estimated cost: 4,671,583.68€
Requested EU contribution: 2,999,018.00€
Kick-off meeting: 15 January 2018, Lund (ESS)
90% of the budget already received
3 months extension due to COVID19 have been requested and obtained
All deliverables ready on time
All milestones achieved on time

## Slide 46: Possible ESSνSB schedule (2nd generation neutrino Super Beam)
2021: End of ESSνSB Design Study, CDR and preliminary costing
2012: inception of the project
2016-2019: beginning of COST Action EuroNuNet
2018: beginning of ESSνSB Design Study (EU-H2020)
2022-2024: Preparatory Phase, TDR
2025-2026: Preconstruction Phase, International Agreement
2027-2034: Construction of the facility and detectors, including commissioning
2035-: Data taking
Nucl. Phys. B 885 (2014) 127

## Slide 47: Near future possibilities for continuation
  Destination 1: INFRADEV-01 : Developing, consolidating and optimizing European RIs landscape by reinforcing RI capacities in Europe. Here we need to make the application to the Horizon Europe Destination #1 significantly different from our previous Horizon 2020 Design Study application, and include implementation studies of ESSνSB on the ESS and Garpenberg sites and a HIFI conceptual study, primarily for low energy nuSTORM and a muon-cooling test-bed for a Neutrino Factory and possibly Muon Collider.
    Deadline: 24 March 2022
    Preparation of the application will start soon
  ERC-Synergy (extensive R&D is allowed): A group of two to maximum four Principal Investigators (PIs) – of which one will be designated as the corresponding PI (cPI) – working together and bringing different skills and resources to tackle ambitious research problems. No Synergy Grant call announced before summer 2021 but foreseen afterwards. Here the first step will have to be to designate at least two PIs. A prerequisite for an ERC Synergy grant is that the PIs have an outstanding track record in scientific research.
    Deadlines not yet clear

## Slide 48: Possible scenario for new near future applications
Possible WPs:
Civil engineering (onsite and offsite) abd safety.
Linac accumulator and race-track.
Target Station, hadron/muon production and muon extraction.
Low Energy nuSTORM.
Detectors and physics performance (synergy between ESSnuSB and LEnuSTORM).
Muons for future. applications, including 6D cooling tests (several locations are possible).

## Slide 49: Conclusion
The ESS proton linac will be soon the most powerful linac in the world.
ESS can also become a neutrino facility (ESSνSB ) with enough protons to go to the 2nd oscillation maximum and increase significantly the CPV sensitivity and precise measurement of δCP.
Large associated detectors have a rich astroparticle physics program.
The European Spallation Source will be ready by 2025, upgrade decisions by this moment.
Rich muon program for future ESS upgrades
  Low energy nuSTORM
  Muon Collider R&D
Excellent conditions for DAR and Coherent Scattering experiments
New applications under preparation

## Slide 50: Backup

## Slide 51: EuroNuNet
COST application for networking: CA15139 (2016-2020)
  EuroNuNet : Combining forces for a novel European facility for neutrino-antineutrino symmetry violation discovery (http://www.cost.eu/COST_Actions/ca/CA15139)
  Major goals of EuroNuNet:
    to aggregate the community of neutrino physics in Europe to study a neutrino long baseline concept in a spirit of inclusiveness,
    to impact the priority list of High Energy Physics policy makers and of funding agencies to this new approach to the experimental discovery of leptonic CP violation.
  13 participating countries
http://euronunet.in2p3.fr/
The members are countries which signed the Action MoU

## Slide 52: ESSνSB at the European level
A H2020 EU Design Study (Call INFRADEV-01-2017)
Title of Proposal: Discovery and measurement of leptonic CP violation using an intensive neutrino Super Beam generated with the exceptionally powerful ESS linear accelerator
Duration: 4 years
Total cost: 4.7 M€
Requested budget: 3 M€
15 participating institutes from 11 European countries including CERN and ESS
6 Work Packages
Approved end of August 2017
ESSνSB
BENE (2004-2008)
ISS (2005-2007)
EUROν (2008-2012)
LAGUNA (2008-2010)
LAGUNA-LBNO (2010-2014)
COST Action CA15139 (2015-2019)

## Slide 53: How the CPV coverage and resolution curves have been produced
T2HK:
  Same curves that Hyper-K has showed at the Neutrino Town Meeting at CERN and the one that was showed at Neutrino 2018.
  Systematics are said by T2HK to be between 3% to 4%.
  sin2 2θ13 =0.1 and θ23= π /2.
DUNE:
  Public globes file released by the DUNE collaboration with the CDR, the only change is to increase the number of years from 7 to 10.
  sin22θ13 =0.1 and θ23=π/2, to be compatible with the T2HK line.
ESSnuSB:
  Instead of considering as usual “Opt. Snowmass errors" it is only assumed an overall 3% systematic error in the different signal and background channels, more in line with T2HK assumptions.
  sin22θ13 =0.1 and θ23= π /2, to be compatible with the T2HK line.

## Slide 54: Beyond DUNE, JUNO, HyperK: ESSνSB, P2O and Neutrino factory
Roumen Tsenov
Department of Atomic Physics, University of Sofia
European Neutrino "Town" meeting and ESPP 2019 discussion, CERN, 24.10.2018

## Slide 55: Systematic errors
Phys. Rev. D 87 (2013) 3, 033004 [arXiv:1209.5973 [hep-ph]]

## Slide 56
ESSνSB 500 kt tank at 540 km.
ESSνSB 500 kt tank at 360 km.
ESSνSB 250 kt tank at 540 km
and 250 kt tank at 360 km.
(degrees)
CPV performance comparison between ESSnuSB, DUNE and Hyper-K
assuming 3% systematic errors for ESSnuSB in line with the other two.

## Slide 57: Fraction of δCP
Lund
Zinkgruvan
(360 km)
Garpenberg
(540 km)
2 active mines aligned…
My personal opinion:
these scenarios are too optimistic for all facilities
(E. Martinez-Fernandez)

## Slide 58: Comparisons
Comparison using the same systematic errors
Phys. Rev. D 87 (2013) 3, 033004 [arXiv:1209.5973 [hep-ph]]

## Slide 59: The ESS neutron facility
rotating tungsten target

## Slide 60: Possible locations for far detector
CERN
ESS
Kongsberg
Løkken
LAGUNA sites

## Slide 61: nuSTORM
Proposed at FERMILAB and CERN (~3.8 GeV muons)
sterile neutrino searches